Research Plan

Rationale: [Number] people die each year in accidents related to distracted driving, [percent]% of which are related to cell phone usage. It would be ideal if a solution were found which could reduce the incidence of poor driving skills including improper phone usage and thus save lives and money.

Research Questions:
- What other solutions have already been proposed to remedy this issue?
- How does operant conditioning tie into designing an effective solution?
- What sorts of behaviors could potentially cause dangerous driving?

Engineering Goal: Design a device which can alert users of potentially poor driving and cause them to cease behaviors which could cause it.

Risk and Safety: The production of the main printed circuit board requires the use of potentially dangerous chemicals such as hydrochloric acid and sodium hydroxide and can potentially produce toxic fumes. Proper lab procedures must be taken and the work must be done in a fume hood.

Hazardous Chemicals (see Risk and Safety):
- Pure NaOH – 1 gram per 1000 milliliters water
- 37% hydrochloric acid
- 3% hydrogen peroxide
- Standard lab procedures and a fume hood should be used to prevent chemical injuries.
- Waste copper (II) chloride is toxic and will be reacted with aluminium metal into aluminium chlorides, which can be diluted and disposed in a drain.

Data Analysis: Prototype design will be judged based on the following criteria:
- Does the prototype function as expected?
- Would it be effective in alerting a user?
- If so, would the device alert the user without presenting an extra distraction or danger?

Instructions for Fabrication of Device

Tools needed:
- Hot plate
- Fume hood
- Nitrile gloves
- Fluorescent lamp
- Aerator stone and aquarium pump
- Frying pan or other crucible
- Soldering iron and solder

Materials needed:
- Copper-clad PCB
- Photoresist dry film
- Sodium carbonate
- Sodium hydroxide (lye)
- Hydrochloric acid (37%)
- Hydrogen peroxide (3%)
- Electronic components
  - Yellow LED
  - Inverter IC (Diodes Incorporated 74AHC1G04SE-7) or NPN transistors (2N2222A)[*]
    [*] The inverter IC is insanely small and frustratingly difficult to use. If needed, use a transistor-based NOT gate instead.
  - Resistors
  - Buzzer
  - Jumper wires
  - Flux and solder paste (used for SMD components)
  - Batteries (3V total)
- Contact switch components
  - HDPE sheets (milk jug material)
  - Aluminium foil
  - Nylon thread and Velcro
- Steering wheel cover
- Project enclosure box

Procedure:
1. Cut a copper clad PCB to fit in a project enclosure.
2. Etch the PCB to receive components.[**]
  [**] Procedure adapted from “DIY PCB using Liquid Photoresist” by synthdood via Instructables (http://www.instructables.com/id/DIY-PCB-using-Liquid-Photoresist/) and “Make Ten Etchants for Copper Printed Circuit Boards” by NurdRage via YouTube (https://youtu.be/Q4tWEse2rDI)
  1. Mask the PCB using photoresist dry film.
  2. Apply a transparency printed with circuit design, toner side down.
  3. Expose the board by placing it near a fluorescent lamp.
  4. Make a developer solution from sodium carbonate (1g Na2CO3 per 1L H2O).
  5. Develop the board by placing it in the sodium carbonate solution for 15 minutes. Do not allow the solution to become too polluted; if it does, replace the solution.
  6. Make an etchant by adding one part hydrochloric acid to two parts hydrogen peroxide.
  7. Etch the board by placing it in the etchant along with air pumped through an aerator stone. Flip the board periodically to ensure even etching.
  8. Drill holes to receive components (if applicable).
  9. Make a stripping solution by mixing three tablespoons of lye with a large frying pan of water. Heat the solution and place the board in it to release any leftover photoresist.
  10. Wash the board to remove any trace chemicals.

1. Refer to the circuit diagram (Figure 1) to attach all components to the etched PCB.
  1. To create the contact switches, glue two pieces of aluminium foil onto a folded sheet of HDPE. Connect each piece of foil to a lead wire. Ensure that the foil connects when pushed together.
2. Mount the circuit board in the project enclosure. Ensure that the indicator LED is visible.
3. Stitch the contact switches to the steering wheel cover in the locations where the hands should rest while driving. Ensure that the folded edge faces the driver.
4. Using Velcro to attach the enclosure box to the steering wheel cover.
5. The device can now be installed on a vehicle by placing it on a steering wheel. (The enclosure may need to be attached after the switches and steering wheel cover have been installed.)