Research Plan

Rationale
In 2013, 424000 people were injured and 3154 were killed in accidents involving distracted drivers, often involving texting or the improper usage of phones. It would be ideal if a solution were found which could reduce the incidence of poor driving skills including improper phone usage and thus save lives and money.

Research Questions:
- What sorts of behaviors could potentially cause dangerous driving?
- What other solutions have already been proposed to remedy this issue?
- How does operant conditioning tie into designing an effective solution?

Engineering Goal
Design a device which can alert users of potentially poor driving and cause them to cease behaviors which could cause it.

Risk and Safety
The production of the main printed circuit board requires the use of potentially dangerous chemicals such as hydrochloric acid and sodium hydroxide and can potentially produce toxic fumes. Proper lab procedures must be taken and the work must be done in a fume hood.

Hazardous Chemicals (see Risk and Safety):
- Pure NaOH
- 37% hydrochloric acid
- 3% hydrogen peroxide
- Standard lab procedures and a fume hood should be used to prevent chemical injuries.
- Waste copper(II) chloride will be regenerated with hydrochloric acid and air to act as an etchant for future testing. When the etchant is no longer needed, it will be reacted with sodium hydroxide to form (after dehydration) copper(II) oxide, which will be reserved.
Data Analysis
Prototype design will be judged based on the following criteria:
- Does the prototype function as expected?
- Would it be effective in alerting a user?
- Can the device be installed with relative ease in existing vehicles?

Instructions for Fabrication of Device

Tools needed:
- Hot plate
- Fume hood
- Nitrile gloves
- Ultraviolet/fluorescent lamp or sunlight
- Aquarium pump and silicone tubing
- Soldering iron and solder
- Clothes iron

Materials needed:
- Copper-clad PCB
- Photoresist dry film
- Solder paste (Sn63/Pb37) and flux
- Sodium carbonate
- Sodium hydroxide, 99% (lye)
- Hydrochloric acid, 37%
- Hydrogen peroxide, 3%
- Electronic components
  - Yellow LED
  - NPN transistors (Diodes Incorporated BC817-16W-7 and 2N2222 TO-18)
  - USB connectors
  - Buzzer
  - Jumper wires
  - Batteries (3V total)
- Contact switch components
  - Stainless steel conductive cloth
  - Wire leads
  - Nylon thread and Velcro
- Steering wheel cover
- Project enclosure box

Procedure:
1. Cut a copper clad PCB to fit in a project enclosure.
2. Etch the PCB to receive components.
  1. Laminate the PCB using photoresist dry film and an iron.
  2. Apply a transparency printed with circuit design negative, toner side down. Hold the mask in place by taping it to the board firmly so no light will leak under the mask.
  3. Expose the board to a UV lamp for 15 minutes until the resist has hardened.
  4. Make a developer solution from sodium carbonate (1g Na2CO3 per 250g H2O).
  5. Develop the board by placing it in the sodium carbonate solution for 15 minutes. Do not allow the solution to become too polluted; if it does, replace the solution.
  6. Make an etchant by adding 133.3 mL of hydrochloric acid to 266.7 mL of hydrogen peroxide.
  7. Etch the board by placing it in the etchant and bubbling air into the solution. Flip the board periodically to ensure even etching.
  8. Drill holes to receive components (if applicable).
  9. Make a stripping solution by mixing 15 grams of sodium hydroxide with 67 grams water. Place the board in it to release any leftover photoresist.
  10. Wash the board to remove any trace chemicals.
  11. Paint over the board using solder mask paint.
  12. Apply a transparency printed with a positive image of the design (solder pads only), and expose to a UV radiation source. Remove unhardened paint using turpentine.
3. Attach all components to the PCB. Use a hot plate to reflow the solder.
  1. The leaded solder will melt around 185 degrees C. Care must be taken to not damage the board or components due to excessive heat.
4. Mount the circuit board in the project enclosure. Ensure that the indicator LED is visible.
5. Stitch the conductive cloth in the correct locations on the steering wheel cover. Connect each side to the main board.
6. Using Velcro to attach the enclosure box to the steering wheel cover.
7. The device can now be installed on a vehicle by placing it on a steering wheel. (The enclosure may need to be attached after the steering wheel cover has been installed.)

Handling and Disposing Etchant:
1. Used etchant contains copper(II) chloride, hydrochloric acid, and hydrogen peroxide. Copper(II) chloride also acts as a PCB etchant. This can be strengthened by adding additional copper metal and pumping in air if the hydrogen peroxide is depleted.
2. To dispose of copper(II) chloride when it is no longer needed, sodium hydroxide is added to form copper(II) oxide, which will be reserved (it has its own uses).
Works Cited
Works Cited
"DIY PCB Using Liquid Photoresist." Instructables.com. Autodesk, n.d. Web. 28 Oct. 2015.
"Facts and Statistics." Distracted Driving : Facts And Statistics. US Department of Transportation, n.d. Web. 28 Oct. 2015. <http://www.distraction.gov/stats-research-laws/facts-and-statistics.html>.
"How to Dispose of CuCl2 ?" ScienceForums.net. N.p., 14 Oct. 2012. Web. 01 Nov. 2015. <http://www.scienceforums.net/topic/69730-how-to-dispose-of-cucl2/>.
How to Make PCB Using Photoresist Dry Film. YouTube. Google, 18 May 2014. Web. 28 Oct. 2015. <https://www.youtube.com/watch?v=cRCFGZxmob0>.
Make 10 Etchants for Copper Printed Circuit Boards. YouTube. Google, 8 Dec. 2012. Web. 28 Oct. 2015. <https://www.youtube.com/watch?v=Q4tWEse2rDI&feature=youtu.be>.
Puri, Nitin. "ORIGOSafe Stops Drivers from Texting." ZDNet. CBS Interactive, 20 Mar. 2013. Web. 28 Oct. 2015. <http://www.zdnet.com/article/origosafe-stops-drivers-from-texting/>.